Haskell to Verilog: Preliminary Design
# Objective
To design a program capable of compiling Haskell programs into Verilog modules for use as hardware accelerators.
# Implementation Notes
Will be written in C++ using the Qt libraries (boost may be considered as a possible alternative).
Rust was considered, but was rejected due to immaturity (still in alpha, tooling and documentation are lacking).
# Scope
- Input may be restricted to a subset of Haskell. e.g. don't need to implement functors, monads
- Input should be compatible with existing Haskell compilers, possibly via a compatibility library. (This requirement may be waived if it proves too difficult.)
- May manually implement core functions, or simply compile source from standard library
  - the effort of manual implementation should be weighed against implementing monads, etc.
  - some core functions may need to be implemented manually anyway for performance reasons (e.g. map)
- Type inference will not be implemented. The input will be loaded into a Haskell interpreter and queries performed instead. This also simplifies syntax checking.
- Support for recursion will be limited.
  - Unary tail recursion is guaranteed (can be trivially rewritten as a loop)
  - unary non-tail recursion may be implemented if it proves feasible. This would be expressed as two loops – one to represent function calls raising the call stack, and one to represent returns lowering the call stack. The only state required would be a counter, resulting in a logarithmic space complexity.
  - Non-unary recursion is not feasible. It has an exponential space complexity, and would require a call stack.
# Compilation Process
## Parsing
### Lexical & Semantic Analysis
This step involves the conversion of the Haskell code into an abstract syntax tree (AST). Constructs such as functions will be identified in C++ via their indentation, then passed to a parser generated by Bison and Flex. (Lemon and attoparsec may also be considered as alternatives to Bison + Flex).
### Computational Analysis
The AST will then be converted into a data dependency graph. Each function will be converted individually, then connected to other functions as required. This will result from a simple mapping of Haskell's syntactic constructs, as all functions in Haskell take form of “where the input is in this form, return this”. Loops will form if recursive functions are used.
The code will be partially evaluated to determine which intermediate values are known at compile-time at which depend on inputs. (This can be implemented as a simple breadth first graph traversal.) The graph will be divided into thunks,[1] such that no loops exist within a thunk. Registers will be inserted along the edges that pass between thunks, such that recursion can be performed by clocking the circuit until the data propagates to the output.
[1] In Haskell, a thunk is a unit of work performed when a value is required (Haskell uses lazy evaluation.) I shall use this term to refer to the amount of work performed within a single clock cycle. i.e. between registers.
## Compilation
The data dependency graph will be converted to Verilog via a simple graph traversal. Each thunk will be mapped to a clock-triggered always-block, with data passed between them using registers. Mapping each thunk to a module may simplify the resulting Verilog.
## Optimization
Various optimizations will be implemented once the compiler is functional. Some of them are listed below. While I do not intend to implement all of them, they provide a useful perspective on what enhancements may be possible.
### Loop Vectorization
In the base implementation, each recursive call of a function will be a separate thunk, with the function being implemented within a single module. This is inefficient for simple functions. Chaining together multiple functions within a single thunk (with muxes added to check for boundary conditions) with result in an increase in performance proportional to the no. of instances of the function.
### Automatic Pipelining
Dividing thunks which limit the clock rate could be implemented by parsing the output of a timing analysis performed by Quartus. As this would only improve performance when using an external clock signal, it is a low priority.
### Evaluation of Arrays
The base implementation shall be suitable for computing functions of individual values. A significant improvement to this would be allowing some of those values to be pointers to arrays, such that the arrays would be automatically iterated over. Multiple values could be evaluated in parallel, though this would be limited by the bandwidth of the memory. This is a pre-requisite for the following optimization.
### Intelligent Caching for Image Convolution
As the compiler is aware of the relative addresses used to compute the new value for each pixel, an accelerator-specific cache could be implemented which represented the sub-matrix of pixels. The contents would be shifted one position each cycle, with new values being read in.
It may also be possible to improve upon the order in which the pixels are evaluated in order to maximise cache performance – a survey of academic journals and some simple genetic algorithms should demonstrate if this is feasible.